## Slide 1
Lecture-1
Digital LOGIC DESIGN
UNIT-vi
PROGRAMABLE LOGIC DEVICES
Archana P
  BE(ECE), MTECH(ECE)
Dept of ECE

## Slide 2: Review of Unit-5 : Sequential Circuits-II
The sequential circuit model.
Asynchronous counters
Design of simple synchronous sequential circuits such as counters.
Design of modulo-N counter, Ring counter, twisted ring counter.
Shift registers
Applications: Design of 1010 sequence detector

## Slide 3: Unit-6: Programmable Logic Devices
Basic PLD’s-ROM, PROM, PLA, and PLD
Realization of Switching functions using PLDs.
Algorithmic State Machines: State machines and state diagrams.
Applications: Design of a Weighing machine and Binary multiplier.

## Slide 4: Programmable Logic Devices
A Programmable Logic Device (PLD) is an integrated circuit with internal logic gates that are connected through electronic fuses.
The gates in a PLD are divided into an AND array and an OR array that are connected together to provide an AND-OR sum of product implementation.
The initial state of a PLD has all the fuses intact.
Programming the device involves the blowing of internal fuses to achieve a desired logic function.

## Slide 5: ROM vs. PLA/PAL
(a) Programmable read-only memory (PROM)
Inputs
Fixed
AND array
(decoder)
Programmable
OR array
Outputs
Programmable
Connections
(b) Programmable array logic (PAL) device
Inputs
Programmable
AND array
Fixed
OR array
Outputs
Programmable
Connections
(c) Programmable logic array (PLA) device
Inputs
Programmable
OR array
Outputs
Programmable
Connections
Programmable
Connections
Programmable
AND array

## Slide 6: Read Only Memory(ROM)
Given a 2kx n ROM, we can implement any combinational circuit with at most k inputs and at most n outputs.
k-to-2k decoder will generate all 2k possible minterms
Each of the OR gate implements SOP expression
AND gate array is fixed and OR gate array is programmable.
F0 = ∑ (1,5,7) F1= ∑ (1,4) F2= ∑ (0,7) F3= ∑ (2,5,7)

## Slide 7: Programmable Logic Array(PLA)
AND gate array is programmable and OR gate array is also programmable
The PLA does not provide full decoding of the input variables and does not generate all the minterms. Generates minterms as per the problem requirement.
Product terms are generated by programmable AND array.
Sum Of Products is generated by programmable OR array.

## Slide 8: EX 1: Implement the given functions using PLA F1 = AB’ +AC+A’BC’ F2= AC+BC

## Slide 9: Programmable Array Logic (PAL)
The PAL is a programmable logic device with programmable AND array and fixed OR array.

## Slide 10: EX 1: implement given functions using PAL W= ABC’ +A’B’CD’ X= A+BCD,Y= A’B+CD+B’D’ , Z= ABC’+A’B’CD’+ AC’D’+ A’B’C’D
Programmable Array Logic (PAL)

## Slide 11
W= ABC’ +A’B’CD’
X= A+BCD
Y= A’B+CD+B’D’
Z= ABC’+A’B’CD’+ AC’D’+ A’B’C’D

## Slide 12: ASM CHART
A special flow chart that specifically to define digital hardware algorithms is called ASM chart.
A hardware algorithm is a step by step procedure to implement the desire task
What is the Difference between conventional flow chart and ASM chart
conventional flow chart describes the sequence of procedural steps and decision paths for an algorithm with out concern for their time relationship
An ASM chart describes the sequence of events as well as the timing relationship b/n the states of sequential controller and the events that occur while going from one state to the next.

## Slide 13: Components of ASM Chart
State box:
  A state of a clocked sequential circuit is represented by a rectangle called state box.
  The name of the state is written to the left of the box.
  The binary code assigned to the state is indicated outside on the top right side of the box.
  A list of unconditional outputs is written in the box.

## Slide 14: Components of ASM Chart
2. Decision box:
  The decision box is represented by a diamond shape with one input path and two output paths.
  The outputs are true and false paths.
  The decision box describes the effect of an input on the control subsystem.
  A Boolean variable or input or expression written inside the diamond indicates a condition which is evaluated to determine which branch to take..

## Slide 15: Components of ASM Chart
3.Conditional output box:
  The conditional output box is represented by a n oval with one input path and one output path.
  The outputs that depend on both the state of the system and the inputs are indicated inside the box.

## Slide 16: Salient Features of ASM Chart
ASM chart describes the sequence of events as well as the timing relationship between the states.
ASM chart contains one or more interconnected blocks.
Each ASM block contains exactly one state box together with the decision boxes and conditional output boxes associated with that state.
Every block in an ASM chart specifies the operations that are to be performed during one common clock pulse.
ASM chart block has exactly one entrance path and one or more exit paths represented by the structure of the decision boxes.

## Slide 17: Example ASM chart for MOD-6 counter

## Slide 18: Binary Multiplier
Multiplication Operation Steps
  Bit Q0 of multiplier operand is checked.
  If Q0 bit is one then multiplicand and partial product are added and all bits of C, Aand Q registers are shifted to the right one bit.
  If Q0 bit is 0 then only shift operation is carried out.
  Steps 1 and 2 are repeated n times to get the desired result in the A and Q registers.

## Slide 19: Example Multiplication Operation

## Slide 20: Flow Chart for Multiplier

## Slide 21: ASM Chart for Multiplier

## Slide 22: ASM Chart for Weighing Machine
We want to design a sequential machine which will calculate the weight of a given binary number.
The weight of a binary number is defined as the number of 1s present in its binary representation.